## Slide 1
Product Introduction
www.tendacn.com
--300M Wall Plate AP W6_US

## Slide 2
Agenda
1. Application Scenarios
2.W6 Overview
4.Advices For Sales
3.W6 Main Features

## Slide 3
Application Scenarios
Hotel Guest Room
Dormitory
Villa
Dense room scenarios or high expectation of decoration
1.Eliminate the dead spot and ensure high quality connection in every corner
2. In-Wall design can blend into the existing decoration perfectly

## Slide 4
Agenda
1. Application Scenarios
2.W6 Overview
4.Advices For Sales
3.W6 Main Features

## Slide 5
W6_US is the latest generation wall plate Wi-Fi access point (AP) which can be installed in 120mm US wall jack without breaking the existing decoration. It is well suited to hotel room, villa, university dormitory, hospital wards and other sites with densely divided rooms. It helps mitigate signal quality problems caused by traditional AP deployment in such sites, and greatly reduces capital expenses and operation expenses in running these sites.
What it does.

## Slide 6
Hardware Specifications
Frequency | 2.4GHz
Wireless Rate | Max 300Mbps
CPU | RTL8196-VE3-CG
RF | RTL8192ER
Flash | 4MB
RAM | 32MB
Interface | 2*10/100Mbps
Button | 1*Reset
LED | 1*SYS
Power | PoE 802.3af

## Slide 7
Interface Overview
PoE Out+Data
Speed: 10/100Mbps
Output power: 802.3af Class 2(6.49W)
PoE In+Data
Speed: 10/100Mbps
Input power: 802.3af

## Slide 8
LED & Button Overview

## Slide 9
Product Dimension
L*W(mm) Front Panel
Height(mm)
L*W(mm) Bottom Panel

## Slide 10
Hardware Installation
1.Open the cover plate of W6_US
2. Install W6_US into the wall jack and fix with screws

## Slide 11
Agenda
1. Application Scenarios
2.W6 Overview
4.Advices For Sales
3.W6 Main Features

## Slide 12
1. 120mm US In-Wall Design
Easy to blend into decoration, more aesthetic

## Slide 13
Versatile PoE In+Data LAN Port
PoE Out
Data+PoE passthrough(802.3af class2), more convenient

## Slide 14
3. Advanced Security
WPA2-PSK/WPA2-Enterprise
Client Isolation
SSID Isolation
VLAN For Multi SSID
Multi mechanism, more secure

## Slide 15
4. Performance Optimization Features
Reduce Interference
Ensure the user capacity
on adjacent APs
Forbid weak signal client affect wireless performance
20MHz/40MHz Option
Client Limitation For SSID
RSSI Limitation

## Slide 16
5. Easy To Manage
W6_US can be centralized managed by AP controller M3 to configure it at a single location. You can edit AP’s Device name, SSID, Security key, TX power, Client limitation etc. Also you can view the AP online, client online information after setup.
Easy To Install, Easy To Manage

## Slide 17
Agenda
1. Application Scenarios
2.W6 Overview
4.Advices For Sales
3.W6 Main Features

## Slide 18
WLAN Solution Provider
WORLD WIDE WIRELESS
Area with 120*80mm US Type Wall Jack |  |  |  |  |  |  |  |  | 
Country | America | Brasil | Mexico | Thailand | TaiWan | Phillipine | Australia | Italia | Total
Hotels | 52472 | 16701 | 7305 | 20177 | 2325 | 2842 | 9971 | 86899 | 198692
120mm US Type Wall Jack

## Slide 19
WLAN Solution Provider
WORLD WIDE WIRELESS
Photo |  | 
Model | W6-US | UAP-IW
Wireless Rate | 300Mbps | 150Mbps
Interfaces | 2*FE LAN | 3*FE LAN
TX Power | Max 20dBm | Max 17dBm
WiFi coverage | 2 Guest Room | 1 Guest Room
PoE In | PoE 802.3af (Compliant all PoE switch) | PoE 802.3af (Only compliant Ubiquiti PoE Switch)
PoE Out | Standard PoE 802.3af (6.49W Class 2) | Passive PoE
Work Standalone | Yes | NO
Comparison with UAP-IW

## Slide 20
liuhaiqiang@tenda.cn